Cexmc User's Manual

# Motivation
Program Cexmc (which stands for Charge EXchange Monte Carlo) was used to find best geometry of a physical setup and calculate acceptances of this setup for 2 types of hadronic interactions:
- π⁻p → π⁰n
- π⁻p → ηn
The interactions were studied for different energies of π⁻ in momentum range ~ 400 - 720 MeV/c for π⁰ production and ~ 700 - 730 MeV/c for η production.
The physical setup can have different degrees of freedom (calorimeters are freely moved combining different distances and angles in respect to the target: see Fig.1) and its best geometry is roughly such a configuration when acceptances have maximum values.
Setup acceptances can be calculated using Monte Carlo method. One might define them as a set of numbers that give a fraction of triggered events from the whole number of simulated interactions when output particle is scattered in a given solid angle in the Center of Mass system. Thus setup acceptances are parameterized by angular ranges and strictly bound to physical setup, trigger logic and studied interaction. Knowing setup acceptances makes it possible to find differential cross-sections of the studied interaction.
The value of differential cross-section in a given solid angle can be deduced from experimental data and the value of acceptance for this angle:
{d%sigma} over {d%OMEGA} prop {N rsub{%OMEGA} } over {A sub{%OMEGA} }

where NΩ is number of experimental events registered in a given solid angle and AΩ is calculated value of the setup acceptance for this solid angle.
Despite the program was developed for a concrete physical experiment its structure is flexible enough to support different setup geometries and interaction models. This flexibility is a result of using GDML for description of setup geometry and a special fast simulation engine that provides easy replacement of studied interactions.
# Setup geometry
The physical setup is constructed from a cylindrical liquid hydrogen target with radius 5cm, two calorimeters that make 2 arms of the setup and contain 6x4 sets of CsI crystals, a monitor counter before the target, 2 veto counters before the calorimeters and various target constructive elements. The calorimeters will detect decay products of the output particle (π⁰ or η). The most intensive decay mode for the both particles is 2γ. The 2 arms of the setup are responsible to catch the gammas and collect their energies. The setup is depicted on Fig.1.
The setup is completely described in file lht.gdml. Besides the geometry this file contains information about sensitive volumes using tag auxiliary with attributes auxtype equal to EnergyDepositDetector and TrackPointsDetector. Tag auxiliary with attribute auxtype equal to SensitiveRegion marks a volume where user can define custom production cuts (particularly, setting custom cuts is supported in calorimeters).
Using lht.gdml is not mandatory. In fact, geometry file is set by command /cexmc/geometry/gdmlFile in preinit phase. In principle user can completely change geometry description of the setup, but any description must meat following requirements:
1. A physical volume Target must be defined somewhere: Cexmc relies on this name and regards volume with this name as the target where the simulation takes place.
2. Physical volume Target must be placed in physical volume TargetInnerCover (referenced in CexmcTargetGeometry::GetTargetTransform())
3. The setup must have 2 arms: left and right. The arms contain detectors that collect energies of particles produced in studied interactions. Also, names of physical volumes in the right arm, that was made sensitive volumes, must contain Right.
4. Detectors in the left and right arms must contain physical volumes with names CalorimeterLeft and CalorimeterRight. The calorimeters must correspond to logical volume vCalorimeter which must be replicated into vCrystalRow volumes; in turn vCrystalRow is replicated into vCrystal volumes. Exact number of replicated volumes is not important. All these constraints are referenced in class CexmcCalorimeterGeometry.

Figure 1: the physical setup
# Run modes
Cexmc has 3 major operational modes:
1. Straight mode (or Monte Carlo mode). The program will read preinit and init macros, then calculate acceptances and (optionally) save data in project files. Project files are saved in a directory defined by environment variable CEXMC_PROJECTS_DIR (or in the current directory if it is not defined), name of the project is specified by option -w. Preinit and init macros are set by options -p and -m respectively. In the Straight mode preinit macro must be specified explicitly, as far as desired production model can be instantiated only in preinit phase.
2. Replay mode (or Read project mode). In this mode the program will not use common Geant4's event loop. Instead, it will sequentially read event data from an existing project and pass them into CexmcEventAction::EndOfEventAction(). The read project is specified by option -r. This mode is useful when user wants to recalculate data from an existing project with different conditions (for example with different reconstruction parameters). The results of run can be written again into another project. In fact, user can make long chain of write-read-write runs sequentially tuning different parameters, but validity of results of a long chain run depends on event data verbose level specified in init macro in in-between runs.
3. Show results mode (or Output mode). The program will output various data from an existing project (specified by option -r). Type(s) of data are specified in option -o. For example, to show results of a run user can specify -orun in command line. To show events, geometry and run results user can specify -oevents,geom,run.
There are also 3 different run modes classified by user interaction type:
1. Batch mode. The program will run without any interaction with user.
2. Interactive mode. The program provides an interactive shell. To run in the interactive mode command line option -i must be specified.
3. Graphical Qt mode. This mode is specified by command line option -g.
# Physics list
Cexmc physics list consists of two parts: one of Geant4's reference physics list and a production model provided by user for fast simulation in the target. Both reference physics list and production model are instantiated as template arguments of class template CexmcProductionModelFactory which is defined as
template < typename BasePhysics,
        template < typename > class StudiedPhysics,
        template < typename > class ProductionModel >
class CexmcProductionModelFactory
{
    public:
        static G4VUserPhysicsList * Create(
        CexmcProductionModelType productionModelType );

        static CexmcBasePhysicsUsed GetBasePhysics( void );

    private:
        CexmcProductionModelFactory();
};
Template argument BasePhysics is to be substituted by a reference physics list; argument StudiedPhysics corresponds user's physics and must be implemented as a class template parameterized by a G4VProcess subclass and derived from G4VPhysicsConstructor; argument ProductionModel corresponds user's interaction model: this is a class template parameterized by an arbitrary type (in case of Charge Exchange production model it is parameterized by output particle's type, e.g. π⁰ or η). Production model must inherit class CexmcProductionModel which provides methods to access production model data and methods to set and access triggered angular ranges.
Concrete production model factory is instantiated in CexmcBasicPhysicsSettings.hh:
#ifdef CEXMC_USE_QGSP_BIC_EMY
typedef QGSP_BIC_EMY CexmcBasePhysics;
#else
typedef QGSP_BERT CexmcBasePhysics;
#endif

typedef CexmcProductionModelFactory< CexmcBasePhysics,
        CexmcHadronicPhysics,
        CexmcChargeExchangeProductionModel >
        CexmcChargeExchangePMFactory;

typedef CexmcChargeExchangePMFactory CexmcPMFactoryInstance;
Two reference physics list are supported from the makefile: QGSP_BERT and QGSP_BIC_EMY, they are controlled by macro CEXMC_USE_QGSP_BIC_EMY. If user wants to use a different reference physics list he can edit CexmcBasicPhysicsSettings.hh.
CexmcProductionModelFactory has method Create() which creates and returns an object of class template CexmcPhysicsList instantiated with template arguments supplied by the factory. CexmcPhysicsList inherits reference physics list and CexmcPhysicsManager:
template < typename BasePhysics, template < typename > class StudiedPhysics,
        typename ProductionModel >
class CexmcPhysicsList : public BasePhysics, public CexmcPhysicsManager
{
    public:
        CexmcPhysicsList();

    public:
        CexmcProductionModel * GetProductionModel( void );

        G4bool IsStudiedProcessAllowed( void ) const;

        void ResampleTrackLengthInTarget(
        const G4Track * track,
        const G4StepPoint * stepPoint );

    private:
        StudiedPhysics< ProductionModel > * studiedPhysics;

        G4bool proposedMaxILInitialized;

        G4double proposedMaxIL;
};
Class CexmcPhysicsManager implements a number of methods related to fast simulation model and has interface method GetProductionModel(). Created object is passed as physics manager into constructors of a number of management objects like CexmcEventAction, CexmcRunAction, CexmcTrackingAction and CexmcSteppingAction which enables them to access the production model object.

Figure 2a: electro-magnetic interactions caused by reference physics list
Figure 2b: studied interactions in the target caused by instantiated charge exchange production model
# Fast simulation model
Fast simulation model implements production model simulation in the target. The idea of fast simulation is to make studied interaction occur in the target (and only in the target) as often as possible. Actually it makes them occur almost in every event generated by Geant4 engine. This almost arises from 2 major facts:
1. Not all incident beam particles visit the target (for example, if simulated beam is very wide or a beam particle was scattered and missed the target).
2. There is one important restriction on the distribution of studied interaction vertices: it must be uniform along the beam path in the target. From the point of view of an engine which samples vertices of studied interaction in the target, it means that if geometry of the target makes path length of beam particles depend on position of the particle on the beam projection, then probabilities of interaction sampling must differ for different positions of the particle on the beam projection. For physical setup on Fig.1 particles on left and right edges of vertical projection of a wide beam will only scratch left or right edges of the cylindrical target, and an interaction sampling engine must miss most of interactions for such edgy particles to ensure uniform distribution of interaction vertices in the target.
Many methods related to fast simulation engine are located in classes CexmcPhysicsManager and CexmcStudiedProcess (this class inherits G4WrapperProcess and registers a physical process supplied in template argument of class template CexmcStudiedPhysics in its method ConstructProcess()).
However the most interesting parts occur in CexmcTrackingAction::PreUserTrackingAction() and CexmcSteppingAction::UserSteppingAction(). The PreUserTrackingAction() tags particles which definition match the incident particle of instantiated production model with an object of type CexmcIncidentParticleTrackInfo (derived from G4VUserTrackInformation). This object will hold information related to fast simulation engine for this particle (for example current track length in the target and sampled track length).

Figure 3: uniform distribution of studied interaction vertices in the cylindrical target
Track length is sampled in CexmcPhysicsManager::ResampleTrackLengthInTarget() in PreUserTrackingAction(). This method can be called once again for the same particle in UserSteppingAction() (for example if the particle visits the target second time).
CexmcStudiedProcess watches to sample studied interaction in its method PostStepGetPhysicalInteractionLength(). It returns difference between sampled for this particle track length in the target and current track length the particle already passed. Geant4 uses this value to know when to simulate a physical process that was registered in CexmcStudiedProcess.
# Charge exchange production model
Class CexmcChargeExchangeProductionModel implements the two hadronic models mentioned in the beginning of this document. It inherits G4HadronicInteraction and CexmcProductionModel. The only method it provides is ApplyYourself(). ApplyYourself() uses a phase space generator to generate secondaries and add them to theParticleChange.
There are two phase space generators that user can choose: original cernlib FORTRAN routine GENBOD() and same routine reimplemented in class CexmcReimplementedGenbod. The first choice makes the program depend on FORTRAN libraries and cernlib. The choice are controlled by macro CEXMC_USE_GENBOD; by default CEXMC_USE_GENBOD is not defined.
Implementation of GENBOD() in CexmcReimplementedGenbod was mostly adopted from CERN ROOT class TGenPhaseSpace.
# Hits and Digits

# Physics reconstruction

# Persistency

# Custom filter

# Histograming

# User commands

# Utilities