Cexmc User's Manual

# Motivation
Program Cexmc (which stands for Charge EXchange Monte Carlo) was used to find best geometry of a physical setup and calculate acceptances of this setup for 2 types of hadronic interactions:
- π⁻p → π⁰n
- π⁻p → ηn
The interactions were studied for different energies of π⁻ in momentum range ~ 400 - 720 MeV/c for π⁰ production and ~ 700 - 730 MeV/c for η production.
The physical setup can have different degrees of freedom (calorimeters are freely moved combining different distances and angles in respect to the target: see Fig.1) and its best geometry is roughly such a configuration when acceptances have maximum values.
Setup acceptances can be calculated using Monte Carlo method. One might define them as a set of numbers that give a fraction of triggered events from the whole number of simulated interactions when output particle is scattered in a given solid angle in the Center of Mass system. Thus setup acceptances are parameterized by angular ranges and strictly bound to physical setup, trigger logic and studied interaction. Knowing setup acceptances makes it possible to find differential cross-sections of the studied interaction.
The value of differential cross-section in a given solid angle can be deduced from experimental data and the value of acceptance for this angle:
{d%sigma} over {d%OMEGA} prop {N rsub{%OMEGA} } over {A sub{%OMEGA} }

where NΩ is number of experimental events registered in a given solid angle and AΩ is calculated value of the setup acceptance for this solid angle.
Despite the program was developed for a concrete physical experiment its structure is flexible enough to support different setup geometries and interaction models. This flexibility is a result of using GDML for description of setup geometry and a special fast simulation engine that provides easy replacement of studied interactions.
# Setup geometry
The physical setup is constructed from a cylindrical liquid hydrogen target with radius 5cm, two calorimeters that make 2 arms of the setup and contain 6x4 sets of CsI crystals, a monitor counter before the target, 2 veto counters before the calorimeters and various target constructive elements. The calorimeters will detect decay products of the output particle (π⁰ or η). The most intensive decay mode for the both particles is 2γ. The 2 arms of the setup are responsible to catch the gammas and collect their energies. The setup is depicted on Fig.1.
The setup is completely described in file lht.gdml. Besides the geometry this file contains information about sensitive volumes using tag auxiliary with attributes auxtype equal to EnergyDepositDetector and TrackPointsDetector. Tag auxiliary with attribute auxtype equal to SensitiveRegion marks a volume where user can define custom production cuts (particularly, setting custom cuts is supported in calorimeters).
Using lht.gdml is not mandatory. In fact, geometry file is set by command /cexmc/geometry/gdmlFile in preinit phase. In principle user can completely change geometry description of the setup, but any description must meat following requirements:
1. A physical volume Target must be defined somewhere: Cexmc relies on this name and regards volume with this name as the target where the simulation takes place.
2. Physical volume Target must be placed in physical volume TargetInnerCover (referenced in CexmcTargetGeometry::GetTargetTransform())
3. The setup must have 2 arms: left and right. The arms contain detectors that collect energies of particles produced in studied interactions. Also, names of physical volumes in the right arm, that was made sensitive volumes, must contain Right.
4. Detectors in the left and right arms must contain physical volumes with names CalorimeterLeft and CalorimeterRight. The calorimeters must correspond to logical volume vCalorimeter which must be replicated into vCrystalRow volumes; in turn vCrystalRow is replicated into vCrystal volumes. Exact number of replicated volumes is not important. All these constraints are referenced in class CexmcCalorimeterGeometry.

Figure 1: The physical setup
# Run modes
Cexmc has 3 major operational modes:
1. Straight mode (or Monte Carlo mode). The program will read preinit and init macros, then calculate acceptances and (optionally) save data in project files. Project files are saved in a directory defined by environment variable CEXMC_PROJECTS_DIR (or in the current directory if it is not defined), name of the project is specified by option -w. Preinit and init macros are set by options -p and -m respectively. In the Straight mode preinit macro must be specified explicitly, as far as desired production model can be instantiated only in preinit phase.
2. Replay mode (or Read project mode). In this mode the program will not use common Geant4's event loop. Instead, it will sequentially read event data from an existing project and pass them into CexmcEventAction::EndOfEventAction(). The read project is specified by option -r. This mode is useful when user wants to recalculate data from an existing project with different conditions (for example with different reconstruction parameters). The results of run can be written again into another project. In fact, user can make long chain of write-read-write runs sequentially tuning different parameters, but validity of results of a long chain run depends on event data verbose level specified in init macro in in-between runs.
3. Show results mode (or Output mode). The program will output various data from an existing project (specified by option -r). Type(s) of data are specified in option -o. For example, to show results of a run user can specify -orun in command line. To show events, geometry and run results user can specify -oevents,geom,run.
There are also 3 different interactivity modes:
1. Batch mode. The program will run without any interaction with user.
2. Interactive mode. The program provides an interactive shell. To run in the interactive mode command line option -i must be specified.
3. Graphical Qt mode. This mode is specified by command line option -g.
# Physics list

# Fast simulation model

# Charge exchange production model

# Hits and Digits

# Physics reconstruction

# Persistency

# Custom filter

# Histograming

# User commands

# Utilities